## Slide 1
LAB IV

## Slide 2
Part I - 8-Bit T Flip-Flop Counter
Built an 8-bit synchronous counter from eight T flip-flops.
Each higher bit toggles only when Enable and all lower order count bits are high.

## Slide 3
Part I - RTL and Simulation
RTL confirms the the T flip-flop counter. Simulation was used to verify clear, enable, and counting behavior.

## Slide 5
Part II - 16-Bit Behavioral Counter
Implemented a 16-bit synchronous counter behaviorally using Q <= Q + 1 with enable and active-low clear.

## Slide 6
Part II - RTL and Performance
The counter synthesized to 18 logic elements and 16 registers. The measured Fmax was 396.35 MHz.

## Slide 8
Part III - LPM 16-Bit Counter
Generated a 16-bit LPM_COUNTER with count enable and synchronous clear using the Quartus IP.

## Slide 9
Part III - LPM Configuration and RTL
The LPM counter synthesized to 18 logic elements and 16 registers with an Fmax of 438.79 MHz,
higher than the behavioral implementation.

## Slide 11
Part IV - 0-9 One-Second Counter
Used the 50 MHz board clock with a one-second enable pulse to the digit goes from 0 through 9 once per second.

## Slide 12
Part IV - Counter Implementation
Counter_1Hz generates the one-second enable while Digit_Counter goes from 9 back to 0.
The FPGA clock remains as 50 MHz clock.

## Slide 14
Part V - Scrolling HELLO
Extended the one-second counter concept to scroll HELLO across the seven-segment displays.

## Slide 15
Part V - HELLO Display Implementation
Hello_Scroll controls the display position while Hello_Display maps H, E, L, L, O to active-low across HEX7–HEX0.

## Slide 17
Conclusion
This lab compared the behavioral and LPM counter implementations. RTL Viewer and timing reports were used to be able to analyze each design, while the DE10-Lite board verified the 0-9 one-second counter and scrolling HELLO display. The LPM implementation got the highest measured Fmax of the 16-bit counters.