## Slide 1
LAB III

## Slide 2
Part I - Gated RS Latch
Implemented a gated RS latch

## Slide 3
Part I - RTL and Technology Map
RTL verifies the cross-coupled latch logic; the Technology Map shows the four preserved combinational logic cells.

## Slide 4
Part II - Gated D Latch
Converted the RS latch into a D latch by using D and its complement to generate the gated S and R inputs.

## Slide 5
Part II - RTL and Technology Map
The D latch is transparent when Clk = 1 and holds its previous value when Clk = 0.

## Slide 6
Part III - Master-Slave D Flip-Flop
Built the flip-flop from two D latches: the master uses the inverted clock and the slave uses the normal clock.

## Slide 7
Part III - Master and Slave Latches
RTL and Technology Map both show the two latch stages connected in series to form an edge-triggered storage element.

## Slide 8
Part IV - Latch and Edge-Triggered Flip-Flops
Behavioral Verilog was used to compare a gated latch, positive-edge flip-flop, and negative-edge flip-flop.

## Slide 9
Part IV - RTL and Technology Map
Qa is implemented as a latch, Qb as a positive-edge register, and Qc as a negative-edge register.

## Slide 10
Part V - 8-Bit Register
The register captures SW[7:0] on KEY1 and clears asynchronously when active-low KEY0 is pressed.

## Slide 11
Part V - Register and 7-Segment Displays
HEX1–HEX0 show the current switch value; HEX3–HEX2 show the stored register value. The Technology Map shows eight flip-flop bits.

## Slide 12
Testing and Observations
Part I – SW0=S, SW1=R, SW2=Clk, LEDR0=Q. Set, hold, and reset behavior worked.
Part II – SW0=D, SW1=Clk. Q followed D while Clk was high and held while Clk was low.
Part III – SW0=D, SW1=Clk. Output updated at the clock transition rather than continuously following D.
Part IV – LEDR0=Qa, LEDR1=Qb, LEDR2=Qc. The three outputs showed latch, positive-edge, and negative-edge behavior.
Part V – KEY1 clocked the register, KEY0 reset it, HEX1–0 showed current B, and HEX3–2 held stored A.

## Slide 13
Conclusion
This lab demonstrated the progression from basic latches to edge-triggered flip-flops and registers. RTL Viewer was used to confirm the intended logic, Technology Map Viewer was used to inspect FPGA implementation, and each design was tested on the DE10-Lite board.