## Slide 1
LAB VI

## Slide 2
Lab VI - UART Overview
PC / PuTTY
LC234X USB-UART
async_receiver
FSM + 5 s counter
char2seg
HEX0
LEDR[7:0]
async_transmitter
USB
RXD
byte + ready
echo byte
TXD
The DE10-Lite receives the 8 bit ASCII characters from PuTTY at a 115200 baud. The received byte is then echoed backwards to show on the LEDR[7:0], HEX0, and held by the FSM until the five-second timer ends

## Slide 3
Async_receiver Explanation
Idle
Start
D0
D1
D2
D3
D4
D5
D6
D7
Stop
Synchronize RX input
Sample bits at 8x baud
Shift 8 bits into RxD_data
Check stop bit & pulse ready
The receiver watches for the low start bit, samples the eight UART data bits first, and checks the high stop bit. When a byte is complete then RxD_data keeps the character and RxD_data_ready pulses for one clock cycle

## Slide 4
Async_transmitter Explanation
TxD_start + TxD_data
Load 8 bit shift register
Baud tick 115200
Start + 8 data + 2 stop bits
TxD GPIO[33]
UART frame: start -> bit 0 -> bit 1 -> ... -> bit 7 -> stop 1 -> stop 2
When TxD_start is started, the transmitter loads the TxD_data and sends a UART frame. The receiver ready pulse starts the transmitter, so each character is sent back to the PC as an echo

## Slide 5
char2seg Explanation
8-bit ASCII character
converted to lowercase
case table selects segment pattern
active-low HEX0[7:0]
Character
ASCII
HEX0 pattern
H
0x48
10001001
char2seg is a combinational logic that maps ASCII codes to the DE10-Lite active-low seven segment display. Letters are approximated because a seven-segment display cannot make every letter exactly

## Slide 6
FSM Explanation
IDLE Display blank
HOLD Display character
rx_ready = 1 capture rx_data
timeout = 1 clear display
New rx_ready while in HOLD: update character + restart timer
No rx_ready in IDLE: remain blank
The FSM has two states. IDLE waits for a character while HOLD keeps that character on the LEDs and HEX0. A new character replaces the old one and restarts the timer; when timeout is triggered, the display is cleared and the FSM returns back to IDLE

## Slide 7
5-Second Counter Explanation
50,000,000 clocks / second × 5 seconds = 250,000,000 clock cycles
50 MHz MAX10_CLK1_50
28-bit counter 0 -> 249,999,999
done = 1 at terminal count
FSM clears display
2²⁷ = 134,217,728 < 250,000,000 < 2²⁸ = 268,435,456
So, a 28 bit register is needed.
The timer uses the original 50 MHz board clock rather than creating a new clock so clear resets the count when the FSM is idle or when a new UART character is pressed, so every new character receives a fresh five-second display interval

## Slide 8
UART Hardware Setup and PuTTY
PuTTY: Serial, COM14, 115200 baud
LC234X UART connected to DE10-Lite GPIO
The PC communicates through the LC234X USB-UART adapter. FPGA RX is GPIO[35] and FPGA TX is GPIO[33]. PuTTY is configured for the adapter COM port14 at 115200 baud.

## Slide 9
Character Receive and Display Verification
H
5
C
Multiple characters were sent from PuTTY and correctly showed on the HEX0. LEDR[7:0] also showed the ASCII byte in binary.

## Slide 10
FSM and 5-Second Timeout Verification
Character displayed
Display cleared automatically
timeout
The working system two clips show a received character being held on HEX0 and then automatically clearing after the timer interval. This verifies the HOLD-to-IDLE FSM transition and the five-second counter behavior on the DE10-Lite

## Slide 11
Conclusion
This lab used UART on the DE10-Lite using Verilog. The async_receiver converted the data from PuTTY into an 8-bit ASCII byte, while the async_transmitter returned the data. Char2seg converted the received character for HEX0 and LEDR[7:0] showed the byte in binary. A two-state FSM and a 28-bit counter were made so each received character stayed on for about five seconds before the display cleared. Hardware testing showed multiple characters on HEX0 and confirmed that the timed display turned off automatically.